## Slide 1: Liquid Architectures: Linux on rVEX
Joost J. Hoozemans – Computer Engineering, TU Delft
Thursday, 08 October 2015

## Slide 2: Liquid Architectures
Run-time adaptivity of computing systems (processors, memories, network-on-chips)
to meet changing requirements
of applications being executed
in different environments
A Definition

## Slide 3: Liquid Architectures
Implementing a system that constantly optimizes its hardware for all its running tasks
Vision

## Slide 4: Old days
Homogeneous multicores

## Slide 5: Current state-of-the-art
Heterogeneous multicores

## Slide 6: Dynamic r-VEX core (2015)

## Slide 7: ρ-VEX
VEX: Design-space exploration tool for VLIW processors
Parameters
  Issue width
  Number of registers
  Number of Functional Units (ALU, ...)
Simulation system
Origins

## Slide 8: ρ-VEX
ρ-VEX: VHDL implementation of the VEX ISA
Parametrized
Design-time reconfigurable
  Issue width
  Nr of Functional units
  ISA extensions
Run-time parametrizable
  Issue width
Origins

## Slide 9: ρ-VEX
Thijs van As: version 1.0
Multi-cycle, non-pipelined design
No caches
89 MHz on Virtex 2
Development

## Slide 10: ρ-VEX
Roël Seedorf, Anthony Brandon, Fakhar Anjam: version 2.0
Redesign
Pipelining, forwarding
Dynamic
No caches
117 MHz on Virtex 6
Development

## Slide 11: ρ-VEX
Bhavisha Goel, Me: version 3.0
SoC
caches
75 MHz on Virtex 6
Not dynamic due to
caches
Development

## Slide 12: ρ-VEX
Bhavisha Goel, Me: version 3.0
SoC
caches
75 MHz on Virtex 6
Not dynamic due to
caches
Started with Linux
Development

## Slide 13: ρ-VEX
Jeroen Van Straten: version 4.0
Redesign
Dynamic core, dynamic cache
Generic design (architectural parameters AND pipeline organization)
Precise traps, extensive debugging hardware
75 MHz on Virtex 7
Development

## Slide 14: Dynamic r-VEX core (2015)
Dynamic reconfiguration (5 cycles), multiple context support, cache resizing, snooping cache
Precise interrupts, configuration via memory-mapped registers, dynamic trace unit, support for breakpoints and single stepping through application codes, gdb support, Linux (2.0) running.

## Slide 15: The Need for an Operating System
Leveraging the power of the ρ-VEX

## Slide 16: The need for an Operating System
Reconfigurations need to be controlled
Why do we need an OS?
Notes: So now we have seen that we can optimize our processors hardware for different kinds of programs, as stated in our vision.
The question is; how do we control these reconfigs? We need some kind of program for that.
It needs to know what configuration is best for a program, and change it automatically.
That is where the OS comes in.

## Slide 17: The need for an Operating System
Reconfigurations need to be controlled
Why do we need an OS?
Notes: The OS is a layer between programs and the hardware.
The goal is to have the OS find out what the best hardware configuration for all of its tasks is,
and then run them all as efficiently as possible.

## Slide 18: The need for an Operating System
OS running on ρ-VEX
Restore
Task 2
Save
Task 1
Schedule
t
User
System
Task 2
Task 1
ILP
Notes: This is what an OS is doing all the time. Switching between different task a hundred times per second.
This is how it seems as if all your programs are running at the same time; time sharing.

## Slide 19: The need for an Operating System
OS running on ρ-VEX
Task 1
Task 2
Restore
Task 2
Save
Task 1
Schedule
t
OS can reconfigure the ρ-VEX core during task switch
  Using statically found optimal hardware configurations
  Using performance counters to measure runtime characteristics (NOPs)
Provides optimal configuration for all its tasks
User
System
ILP
Notes: We would like to extend the job of process switching a little bit:
The OS will check the program and see how it is running. It will make a prediction about what configuration will be best when resuming this task.
This prediction can be based on execution phase characterisation found by static analysis by the compiler, but I also plan on designing performance monitoring hardware that measures certain runtime characteristics.
As we can see, Task 1 is a different kind of program than Task 2. It is running on a small core. Task 2 is predicted to be more suitable for a wide core.
Before resuming, the OS should reconfigure the core.

## Slide 20: The need for an Operating System
OS running on ρ-VEX
Task 1
Task 2
Restore
Task 2
Save
Task 1
Schedule
t
User
System
OS can reconfigure the ρ-VEX core during task switch
  Using statically found optimal hardware configurations
  Using performance counters to measure runtime characteristics (NOPs)
Provides optimal configuration for all its tasks
Evaluate
Re-configure
Notes: This is how that would look like.
Of course, there is an enormous amount of challenges involved in this evaluation, prediction, and how and when to do the reconfiguration.
But this is the general idea of how I think we can create our envisioned system.
This also makes it clear why we need to port an operating system to rVEX.

## Slide 21: The need for an Operating System
OS running on ρ-VEX
Task 1
Task 2
Restore
Task 2
Save
Task 1
Schedule
t
User
System
Evaluate
Re-configure
Notes: This is how that would look like.
Of course, there is an enormous amount of challenges involved in this evaluation, prediction, and how and when to do the reconfiguration.
But this is the general idea of how I think we can create our envisioned system.
This also makes it clear why we need to port an operating system to rVEX.

## Slide 22: The need for an Operating System
OS running on ρ-VEX
Task 1
Task 2
Restore
Task 2
Save
Task 1
Schedule
t
User
System
Evaluate
Re-configure

## Slide 23: The need for an Operating System
Task 1
Task 2
Schedule
t
User
System
Re-configure

## Slide 24: Liquid Computing
t
Datapath 1 & 2
Datapath 3 & 4
Datapath 5 & 6
Datapath 7 & 8

## Slide 25: Liquid Computing
t
Task 1
Task 2
Reconf

## Slide 26: Liquid Computing
t
Task 1
Task 2
Reconf

## Slide 27: Liquid Computing
t
Task 1
Task 2
Reconf
Task 5
Task 4
Task 3

## Slide 28: Liquid Computing
t
Task 1
Task 2
Reconf
Task 5
Task 4
Task 3
Reconf
Task 2
Task 3
Reconf
Task 2
Interrupt

## Slide 29: Liquid Computing
t
Task 1
Task 2
Reconf
Task 5
Task 4
Task 3
Reconf
Task 2
Task 3
Reconf
Task 2
5 Cycles!

## Slide 30: Liquid Computing
t
Task 1
Task 2
Reconf
Task 5
Task 4
Task 3
Reconf
Task 2
Task 3
Reconf
Task 2
Goal

## Slide 31: Liquid Computing
t
Task 1
Task 2
Reconf
Current state

## Slide 32: Hardware development
Hardware requirements for Linux

## Slide 33: Hardware development
Processor
Main memory
  Modified Harvard architecture – single address-space
  Adequate size
Serial connection
Trap/Interrupt Facility
Timer
Debugger
  Not strictly required
Requirements
Notes: So what do you need to run an OS?
We need a processor; ok check.
We need memory, preferably a decent amount. rVEX normally uses separate instruction and data memories but we need a single address space.
We want to be able to communicate with the system, to see that it actually does something.
We need the core to be interruptable, and it must be able to handle traps.
We need a timer to generate timer interrupts, because Linux is a time-sharing system.
For efficient debugging, we decided to add a debug unit in hardware (actually the most important reason was that I wanted to know how those things work so I created one for myself)

## Slide 34: Hardware development
Initial platform: GRLIB-based
  Main memory, caches
  UART serial interface for console
  Interrupt controller
  Timer
Additions needed
  Trap facility in the ρ-VEX core
  Debugger
Platform setup
Notes: We started with a platform based on GRLIB, that already met most of the requirements.
We evaluated it and found some additions were needed.

## Slide 35: Hardware development
Platform setup
Notes: Platform overview

## Slide 36: Linux
Adding the VEX architecture to the Linux 2.0 kernel

## Slide 37: Linux
Free, Open source
Runs on 80% of all smartphones
Runs on 80% of all supercomputers
Portable
No MMU? => uCLinux!
  2.0 kernel
Introduction

## Slide 38: Linux
No virtual memory
No memory protection
No paging (also no swapping)
No dynamic stack
Malloc uses global shared memory pool (no brk() )
NO_MMU

## Slide 39: Linux
Components
Only Linux kernel
No applications
Add Arch/code
  Mostly assembly
Notes: What I needed to do, is essentially add Architecture-specific code for my rVEX platform.

## Slide 40: Linux
Created architecture-specific files
  Derived from similar architectures
Write initialization code
Write Interrupt handling code
  Only timer interrupts
Write process switching code
  Fork()
Create and mount root filesystem
System calls
  Partly in libc
Porting steps

## Slide 41: Linux
Architecture-specific code

## Slide 42: Linux
Architecture-specific code

## Slide 43: Linux
Workflow
Write new code
Compile kernel
Run on board
Wait for it to crash
Fix problems
Notes: “Wait for it to crash” was the only part of the whole project that didn’t take a very long time!

## Slide 45: Current/Future work
Simultaneous Multi-Processing
Memory Management Unit
Reconfiguration scheduling algorithms

## Slide 48: The need for an Operating System
Needs a separate processor to run the OS
Inefficient!
ERA – Embedded Reconfigurable Architectures
ρ-VEX
Main processor
Program
Co-processor
Notes: Lets discuss the way this is done currently; The ERA approach.
The system is running the applications on a separate processor. A programmer must manually extract parts of the program to run on the rVEX coprocessor.
The system must then reconfigure the core (if applicable), transfer the program and its data to the core, signal it to start and then wait for it to finish before it can get the result back!
This results in large overheads and is quite inefficient.
This approach has the same drawbacks as hardware-software compilation but without the increased performance.

## Slide 49: Hardware development
Trap/Exception: Anomaly during execution
SPARC-based Vectored Trap controller
  Connects to GRLIB Interrupt controller
VEX Control Registers: VCR
rVEX: “Hardware unavailable” exception
Trap controller
Notes: An interesting option For our rVEX system: a special exception can be created when optimizing the core for minimal area usage.
The OS can decide that some application has not executed a multiply operation for far too long.
It will switch off the unused MUL units or assign them to another core that needs them more.
When the program DOES try to perform a multiplication, this will generate an exception.
Instead of crashing, the operating system will reconfigure the core, WITH MUL units and execution can resume normally. This is future work.

## Slide 50: Hardware development
Trap/Exception: Anomaly during execution
  Interrupts
  System calls
SPARC-based Vectored Trap controller
  Connects to GRLIB Interrupt controller
VEX Control Registers: VCR
Trap controller
Notes: To control the trap unit, I added a new type of register to the register file: control register.
I named them after a needlessly complicated piece of machinery that everyone used to own, but no one knew how to program.

## Slide 51
Flexible hardware:
Solve VLIW drawbacks
  Variable issue-width; minimize NOPs
  Binary compatibility; ρ-VEX can morph into any core design
Increase resource utilization
ρ-VEX : reconfigurable VLIW softcore
Computer Architecture
Notes: To remove these drawbacks, TU Delft has developed a VLIW softcore that is FLEXIBLE.
We use reconfigurable hardware to be able to change the processor design.
The processor has parameters that can be changed. The most important one is the issue-width; this is the number of pipelanes in a processor.
The pipelanes contain the functional units, so this parameter defines how many instructions the processor can execute at the same time.
This removes the drawbacks in the following ways; for applications with low parallelism, we change the core to a small issue width (minimizing NOPs).
For apps with high parallelism, we change the core to a wide issue width (maximizing performance).
Binary compatibility is no problem; a program is compiled for a certain configuration (parameter set). We just change the core to that configuration before starting the program.
So we can SOLVE the VLIW drawbacks using the hardware flexibility we gained from reconfigurable hardware (answering our earlier question).
But theres more. The rVEX is quite unique.

## Slide 52
Computer Architecture
ρ-VEX : reconfigurable VLIW softcore
Notes: Suppose this is your FPGA. There is room to place 8 pipelanes in there (the large squares), and control logic for 4 rVEX cores (the small squares).
We can then configure this into 4 cores with 2 pipelanes each,

## Slide 53
Computer Architecture
ρ-VEX : reconfigurable VLIW softcore
Notes: Or 1 core with 4 pipelanes and 2 cores with 2 pipelanes,

## Slide 54
Computer Architecture
ρ-VEX : reconfigurable VLIW softcore
Notes: Or an 8-issue core or any combination of this.
So if we have a program that does not have much parallelism, we will run it on a 2-issue core. This will save NOPs in the program and allows us to use the rest of the pipelanes for other cores. We can run 3 other programs at the same time!
If we have a scientific application that does matrix calculations, we can run it on an 8-issue core, maximizing performance for that program.
This is the way we are using hardware flexibility to optimize our softcore for a program.